## Slide 1
Physics-Informed Machine Learning Vessel Depth Classification
Roy Michael - Department of Marine Technologies, Haifa University
Physical Model
1. Heave-driven FM source
,
The resulting tonal is broader and less stable.
2. Underwater two-path channel
Background
Passive Acoustic Monitoring can distinguish surface and submerged sources using the effect of wave coupling on mechanical tonal.
3. Surface-source result
FM carrier × dynamic multipath envelope → bandwidth expansion, fading, and reduced persistence.
Surface: overlapping paths cause fading and Doppler spread.
4. Underwater-source result
Stable direct tonal + delayed additive surface echo.
The model predicts broader, less persistent energy for the surface motorboat and narrow, stable tonal bands for submerged DPVs.

## Slide 2
Methodology and Results
Methodology
Signal Ingestion
Estimation Matrix
Feature Extraction
Classification
Results
Dominant spectral peaks
Temporal Stability Separates Depth
Bandwidth separates source depth
Surface motorboat: 136 Hz
Submerged DPVs: 18–26 Hz
Broad spectral distribution vs. narrow tonal bands
Bandwidth Distribution
Spectral Fingerprints of Vessel Depth
Jain’s fairness
Submerged DPV tonal bands persist across longer windows; Surface motorboat stability decreases.
Shannon Entropy stability
Time-in-Band ± 10Hz

## Slide 3
Conclusion and Future Work
Takeaway
Spectral bandwidth and temporal persistence provide complementary, physics-informed cues for distinguishing surface and submerged vessels.
Next steps
Validate across more vessel types, operating conditions, ranges, and environments.
Integrate the features into an ML classifier and real-time detector.
Authors
Roy Michael - Department of Marine Technologies, Haifa University
Prof. Roee Diamant - Department of Marine Technologies, Haifa University
Submerged DPV tonal bands persist across longer windows; Surface motorboat stability decreases.